## Slide 1: COMPUTER ORGANISATION (TỔ CHỨC MÁY TÍNH)
NUMBER SYSTEMS SUPPLEMENTARY NOTES

## Slide 2: Acknowledgement
The contents of these slides have origin from School of Computing, National University of Singapore.
We greatly appreciate support from Mr. Aaron Tan Tuck Choy for kindly sharing these materials.

## Slide 3: Policies for students
These contents are only used for students PERSONALLY.
Students are NOT allowed to modify or deliver these contents to anywhere or anyone for any purpose.

## Slide 4: Recording of modifications
Currently, there are no modification on these contents.

## Slide 5: NUMBER SYSTEMS SUPPLEMENTARY NOTES
Complements
Floating-point Numbers

## Slide 6: COMPLEMENTS (1/3)
“Find the complement of a number” or “complement a number” is the short way of saying… “find the negated value in that complement system”.
For example, the two questions below are equivalent.
  [4-bit] Find/get the 1’s complement of 0110 (or, 1’s complement this value: 0110) Answer: 1001.
  [4-bit] If x is 01101s, what is -x in 1’s complement form? Answer: 10011s
So, “find the 1’s complement of 0110” is not asking for “how is 0110 represented in 1’s complement”. See next two slides for more examples.

## Slide 7: COMPLEMENTS (2/3)
More examples:
  [8-bit] Find the 1’s complement of 101. Answer: 11111010
  [8-bit] Find the 1’s complement of 11001000. Answer: 00110111
  [8-bit] How is 1012 (510) represented in 1’s complement? Answer: 000001011s
  [8-bit] How is -1012 (-510) represented in 1’s complement? Answer: 111110101s
  [8-bit] Find the 2’s complement of 111000. Answer: 11001000
  [12-bit] Find the 2’s complement of 101. Answer: 111111111011

## Slide 8: Difinition
Generally, there are two types of complement of Binary number: 1’s complement and 2’s complement.
To get 1’s complement of a binary number, simply invert the given number. For example, 1’s complement of binary number 110010 is 001101.
To get 2’s complement of binary number is 1’s complement of given number plus 1 to the least significant bit (LSB). For example 2’s complement of binary number 10010 is (01101) + 1 = 01110.
Notes: Binary Number System is one the type of most popular Number Representation techniques that used in digital systems. In the Binary System, there are only two symbols or possible digit values, i.e., 0 (off) and 1 (on). Represented by any device that only 2 operating states or possible conditions.

## Slide 9: Ligical circuit of 2’s complement

## Slide 10: COMPLEMENTS (3/3)
More examples:
  [8-bit] What is 1112 (710) in 2’s complement form? Answer: 00000111
  [8-bit] What is -1112 (-710) in 2’s complement form? Answer: 11111001
  [10-bit] What is 1410 in 1’s complement form? Answer: (0000001110)1s
  [10-bit] What is -1410 in 2’s complement form? Answer: (1111110010)2s

## Slide 11: FLOATING-POINT NUMBERS (1/2)
Assume a 10-bit floating-point scheme with: 1-bit sign, 5-bit normalised mantissa, and 4-bit exponent.
What is this value: 1 11000 1001 ?
Sign bit is 1, so value is negative.
Mantissa is 0.110002, or 0.7510
What about exponent 1001?
  If exponent is unsigned, then exponent = 9
  If exponent is signed, and sign-and-magnitude is used, then exponent = -1
  If exponent is signed, and 1’s complement is used, then exponent = -6
  If exponent is signed, and 2’s complement is used, then exponent = -7

## Slide 12: FLOATING-POINT NUMBERS (2/2)
Therefore,
  If exponent is unsigned, then value is -0.112  29, or -1100000002, or -38410.
  If exponent is in sign-and-magnitude, then value is -0.112  2-1, or -0.0112, or 0.37510.
  If exponent is in 1’s complement form, then value is -0.112  2-6, or -0.000000112.
  If exponent is in 2’s complement form, then value is -0.112  2-7, or -0.0000000112.
1 11000 1001

## Slide 13: Q&A